## Slide 1: ALERT – Addressing Research Gaps in Radio Frequency Machine Learning
Philip Leong (philip.leong@sydney.edu.au)
Notes: Title: ALERT – Addressing Research Gaps in Radio Frequency Machine Learning
Speaker: Prof Philip Leong, School of Electrical and Computer Engineering, The University of Sydney
Abstract: Advances in software-defined radio and deep learning (DL) have enabled radio signals to be detected and classified more accurately than using conventional digital signal processing techniques. However, gaps in radio frequency machine learning (RFML) research regarding suitable Algorithms, Latency, Edge implementations, Representation and Training (ALERT) techniques remain. In the Computer Engineering Laboratory at the University of Sydney, we have been designing FPGA-based accelerators for cyclostationary signal processing and low-precision edge-based training for RFML applications. This talk elaborates on the research gaps and our efforts to address them.
Biography: Philip Leong (梁恆惠) received the B.Sc., B.E. and Ph.D. degrees from the University of Sydney. 1993 he was a consultant to ST Microelectronics in Milan, Italy working on advanced flash memory-based integrated circuit design. From 1997-2009 he was with the Chinese University of Hong Kong. He is currently Professor of Computer Systems in the School of Electrical and Computer Engineering at the University of Sydney, Chief Technology Advisor to ClusterTech, Chief Technology Officer at CruxML and Chief Executive Officer at TernaryNet.

## Slide 2: Acknowledgment of Country
I acknowledge the Gadigal people of the Eora Nation as the traditional custodians of the land on which the university stands and pay respects to Elders past, present and emerging.

## Slide 3: Australia vs Taiwan
More than 200x larger than Taiwan
Population about the same
  27.0M vs 23.4M in 2023

## Slide 4: Computer Engineering Lab
Introduction
CEL focuses on how to utilise parallelism to solve computing problems
  Novel architectures, applications and design techniques
Notes: 1.Differemce with bfp
2. No BM training

## Slide 5: Radio Frequency Machine Learning
Processing RF signals remains a challenge
ML offers an opportunity to achieve RF scene understanding
Overall research theme is to achieve high performance in RFML using FPGAs through (EPIC)
  Exploration, Parallelism, Integration, Customisation

## Slide 6: Collaborators
AMD/Xilinx, Intel
Main Sequence Ventures
Australian Economic Accelerator (AEA)

## Slide 7: Outline
Opportunities for RFML on FPGAs
Features (Cyclostationary Signal Processing)
Training at the edge (Block Minifloats)
Current Work

## Slide 8
1. Opportunities for FPGAs in RFML

## Slide 9: What is an FPGA?
User-customisable integrated circuit
Routing
Dedicated blocks
Input and output blocks
Configurable logic blocks
* Clocking Resources

## Slide 10: Requirements for RFML
Requirements
  High throughput, low latency, good accuracy, integration
Some research gaps (ALERT)
  Algorithms
  Latency
  Edge
  Representations (features)
  Training (to adapt to changing conditions)

## Slide 11: Some Ways to Bridge Gaps
Algorithms: lower complexity techniques with minimal accuracy reduction
Latency: highly pipelined architectures, quantisation, hardware-friendly DNN techniques
Edge: single-FPGA solutions that reduce off-chip communications and utilise massive on-chip bandwidth, integration, memory footprint reduction
Representations: techniques that match properties of signals, e.g. complex numbers, man-made modulation schemes
Training: systems that can adapt to changing conditions

## Slide 12: ALERT Algorithms: Sparse FFT [1]

## Slide 13: ALERT Latency: PolyLUT-Add [2]
https://github.com/bingleilou/PolyLUT-Add
Each neuron implemented in a single LUT

## Slide 14: ALERT Edge: Modulation Classification @ 500 Msps [3]
  Combine quantisation, sparsity and CSE to reduce computation 86%
  Fully pipelined design achieves
  - 488K classifications/s
  - 8 uS latency
https://phwl.org/assets/papers/amc_raw20.pdf

## Slide 15: ALERT Representations: Cyclostationary Features [4]
Cyclostationary: probability distribution changes periodically over time
Excellent at low SNR (but computationally expensive)

## Slide 16: ALERT Training: Training of DNNs at the Edge [5]
Block minifloats which can train with 8 and 6-bit precision
Dataset: ImageNet
Model: ResNet-18
ICML’21 https://openreview.net/forum?id=6zaTwpNSsQ2

## Slide 17: A Vision for RF Scene Understanding
Combine real-time FPGA HW, cyclostationary analysis, ML and AR
Input Length
Cyclostationary Signal Processing (CSP)
10x Acceleration
of CSP in SW (TRL 3)
RF Fingerprinting
on FPGA
ML on FPGA
Apple Vision Pro
Emitter Localization

## Slide 18
2. Representations: Cyclostationary Features [4]

## Slide 19: Cyclostationarity
A time series is said to be cyclostationary if its probability distribution varies periodically with time.
Spectral Correlation Density:

## Slide 20: Introduction
Automatic Modulation Classification (AMC)
  “eyes & ears” of Cognitive Radio
SCD can be used for AMC at low SNR
Training
with SCD
Training
with IQ
J. A. Snoap, J. A. Latshaw, D. C. Popescu and C. M. Spooner, "Robust Classification of Digitally
Modulated Signals Using Capsule Networks and Cyclic Cumulant Features," MILCOM 2022

## Slide 21: Contribution
First high-performance SCD estimation on Versal platforms using the FAM and SSCA techniques.
Fully reproducible designs and results*.
First AIE-only FAM implementation
  Uses only 35% of AIEs
  Requires zero PL resources → RFML + ML integration
First FPGA-accelerated SSCA implementation
  Uses decomposed FFT + PL transpose
  Handles ~1M sample window sizes efficiently
*: https://github.com/Jingyi-li/SCD_VCK5000

## Slide 22: Spectral Correlation Density (SCD)
FFT Accumulation Method (FAM)
Strip Spectral Correlation Analyzer (SSCA)
  Challenge:
  High computational complexity makes it difficult to use in real-time applications.
Notes: The FFT accumulation method (FAM) is am efficient way to estimate the spectral correlation density (which we will refer to as the SCD) using the Fourier Transform. The bandpass filters are implemented using an FFT, after which decimation and downconversion are applied. A second FFT is used to compute the final SCD output. The alpha profile is a 1-dimensional version of the SCD in which the maximum value of cyclic frequency is computed.
The FAM is computationally expensive making it difficult to apply in real-time applications.

## Slide 23: AMD/Xilinx Versal ACAP Architecture
400 AIE processors
20GFLOPS/s = 1.25GHz x 8MACs/cycle x (add+multi)
8TFLOPS/s
Notes: The AMD/Xilinx Versal ACAP architecture (Versal architecture), which merges general-purpose CPUs, programmable logic (PL), and AI Engine (AIE) processors optimised for AI and machine learning optimisation. With 400 AIE processors executing at a maximum 1.25 GHz, capable of delivering 8 MACs/cycles for 32-bit floating-point data, it has peak performance of 8 tera floating point operations per second (TOPS). It turns out the 64K memory is the main constraint for our work.

## Slide 24: FAM & SSCA
FAM
SSCA
: input window size
: Channelizer factor
: Decimation factor
: Size of Second FFT
Mapping:
Mapping:
Nonuniform frequency resolution
Decimation
Computationally efficient
AIE-only implementation
Uniform frequency resolution
Memory limitation
FPGA implementation integrated DDR-PL-AIE

## Slide 25: AIE-only FAM Implementation
FAM consists of 3 stages
  Framing, Demodulate, and FFT2

## Slide 26: Parallelism for FAM
Transpose
Broadcast

## Slide 27: SSCA Implementation
Compute Decomposition
  Common factor map decomposition FFT  Reduce memory requirements
Memory Access & Scheduling
  Ping-Pong buffer  Overlap load/store and compute
  Tiling strategy  Minimize strided DDR access
Throughput & Latency Improvement
  Leverage pipeline execution across FFT stages
  Design dataflow architecture for maximum concurrency
  Minimize inter-core synchronization overhead

## Slide 28: Common Factor Map Decomposition FFT
N-point FFT

## Slide 29: SSCA_2DFFT on Versal
Ping-Pong Buffer
2DFFT
CDP
Tiling Strategy
1st
2nd
Pipeline
Dataflow
CDP: II = data stream in
Parallel CDP
Parallel
Notes: What CDP is

## Slide 30: Results (1)
FAM | SSCA
FAM | SSCA
Single Precision: FAM 9.94e-5, SSCA 1.08e-6
 | PL |  |  |  | AIE Array | 
 | Register | LUT | BRAM | URAM | AIE tile | PLIO
Total Resources | 1,739,432 | 860,336 | 933 | 463 | 400 | -
FAM | 113,686 (6.61%) | 107,601 (12.73%) | 37 (3.97%) | 0 (0.00%) | 137 (34.25%) | 130
SSCA_2DFFT | 15,475 (0.89%) | 11,824 (1.37%) | 349 (37.41%) | 192 (41.47%) | 15 (3.75%) | 13
Notes: Floating point computing

## Slide 31: Results (2)
 | FAM |  | SSCA | 
 | Time | Speedup | Time | Speedup
CPU | 0.194s | 1 | 11.3a | 1
GPU | 2.791ms | 69.51 | 217ms | 52.07
VCK5000 | 0.630ms | 307.94 | 114ms | 99.12
 | FAM_ZCU111[1] | FAM_VCK5000 | SSCA_2DFFT_VCK5000
Input window size | 2,048 | 2,048 | 1,048,576
Initiation Interval (ms) | 0.164 | 0.63 | 114
Throughput (MS/s) | 12.50 | 3.25 | 9.21
Computational Performance (GPOS) | 460 | 189 | 88
Board Power (W) | 35 | 40 | 31
[1] “Fixed-point FPGA implementation of the FFT accumulation method for real-time cyclostationary analysis” ACM Trans.

## Slide 32: Summary
This work enables integration of software defined radio, cyclostationary and ML on a single device for cognitive radio applications
Presented open-source, efficient implementations of the FAM and SSCA techniques on Versal ACAP
  FAM uses 34% of AIE resources and 12% of LUTs
  First reported SSCA implementation N=1M uses 4% AIE and 1% LUTs

## Slide 33
3. Training: FPGA-based Block Minifloat Training Accelerator for a Time Series Prediction Network [5]

## Slide 34: Motivation (1)
What can we do to reduce the energy cost?

## Slide 35: Motivation (2)
Introduction
Target problem: Training on Edge
  Potential: adapt to local conditions
  Problem: ~3x memory and compute vs. inference
  Solution: Use custom number system

## Slide 36: Block Minifloat (BM)
BM = minifloat + shared exponent bias β
minifloat: small floating-point format (same idea as Microscaling MX)
Itroduction
M
M
M
M
M
M
M
M
M
M
M
M
Minifloat
Fixed
BFP
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
E
E
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
M
E
E
E
E
Block Minifloat and Microscaling (MX)
Notes: 1.Differemce with bfp
2. No BM training

## Slide 37: Block Minifloat (BM)
BM = minifloat + shared exponent bias β
minifloat: small floating-point format (same idea as Microscaling MX)
Itroduction
Notes: 1.Differemce with bfp
2. No BM training

## Slide 38: Previous Work: BM-Theory (ICLR21)
Introduction
38
Model: ResNet-18 Dataset: ImageNet
  BM units are:
  Smaller
  Consume less Power
Notes: 1.Differemce with bfp
2. No BM training

## Slide 39: Previous Work: BM-based TL (ICCAD23)
Introduction
39
Transfer learning example from CIFAR-100 to CIFAR-10
Notes: 1.Differemce with bfp
2. No BM training

## Slide 40: This Work
Introduction
BM arithmetic
  Block size: A novel technique for cross-block BM matrix multiplication
  Mixed precision: BM GEMM kernel with runtime configurable precision for FW/BP with pipeline optimization
  DSP packing: 4-bit BM MAC unit with 6 multiplication packed per DSP
Training accelerator
  First implementation of 4-bit BM training for time series network (NBEATS)

## Slide 41: Block size & mixed precision in BM Matrix multiply
Introduction
Block size
(mixed precision)
Accuracy
Problem:
  Block size ≠ tile size
  Computation error in cross-block MM
  Runtime configurable precision GEMM
PE array
Shared exponent

## Slide 42: Cross-block BM matrix multiplication
BM arithmetic
Step 1: Inner product
  Integer based inner-product
Notes: Rounding error: 1) FMA implemented in integer 2) Psum is given extra tailing bit to reduce truncation error 3) only normalize once to avoid conversion rounding error

## Slide 43: Cross-block BM matrix multiplication
BM arithmetic
Step 2: Normalization
  Find maximum in the block
  Norm: Convert to C
  Adjust shared exponent β

## Slide 44: PE -- scalar inner-product computation
BM arithmetic
Mixed precision
  A mixed-precision decoder in minifloat input
  Selectable boundary thresholds in Norm block (Next page)
PE design of GEMM kernel

## Slide 45: BM GEMM kernel
BM arithmetic
PE array
(inner-product)
Normalization
inner-product
Find Maximum
norm
Pipelined implementation
  Inter block & Intra-Normalization Pipeline

## Slide 46: DSP packing
BM arithmetic
DSP packed PE optimized for 4-bit BM training
  Each PE has 2*3 input, 6 MAC unit
  6 Significand multiplication in MAC mapped to one DSP48E2
  Support different precisions during training
DSP packed PE design for 4-bit BM MAC
Bit Arrangement in Different Training Phases

## Slide 47: Time series prediction network - NBEATS
Training accelerator
NBEATS: A time series prediction network with regular architecture (FC layer & residual)
SOTA accuracy result on M3, M4 and statistics benchmark
network
NBEATS block

## Slide 48: NBEATS training accelerator
Training accelerator

## Slide 49: BM GEMM
Experiment
(a) Block size configuration
Block size has small impact on GEMM area

## Slide 50: NBEATS training accuracy
Experiment
Smaller block size, high precision residual, Mixed precision improves accuracy

## Slide 51: NBEATS training accelerator
Experiment
BM4-mixed packed
  Accelerator achieves 779 Gops throughput, DSP utilization 0.7 Gops/DSP (SOTA), power efficiency 42.4 Gops/W (3.1x)
 | Ours (no packing) | Ours (packing) | GPU
Device | Alveo U50 |  | GTX 1080
Process | TSMC 16nm |  | 
Num system | BM4-mixed | BM4-mixed | FP32
Freq.(MHz) | 183 | 159 | 1733
Tput. (Gops) | 299.03 | 779.12 | 2991
Power(W) | 20.86 | 18.38 | 220
Gops/W | 14.34 | 42.4 | 13.6
Gops/DSP | 0.27 | 0.71 | -

## Slide 52: Summary
Demonstrated FPGA-based 4-bit training of time series prediction networks with minimal impact on accuracy
  Systolic array that combines mixed precision and DSP packing
  3x Gops/W in same technology as GPU
Suitable for edge-based systems with modest energy resources

## Slide 53
4. Current Work

## Slide 54: ONRG Understanding Deep Learning-based RFF
Create dataset generators where physical mechanisms can be controlled. Collect OTA data.
Understand how tx and channel imperfections affect the activations of a DL-RFF via XAI.
Test hypothesis: XAI + systematic study of hardware impairments and channel models can improve robustness and model interpretability.
With Kanchana Thilakarathna

## Slide 55: AEA Decreasing Precision Trend

## Slide 56: AEA Ternary Neural Network

## Slide 57: Spinoff Companies
Real-time AI Applications
on FPGAs
Fabless Semiconductor Company
TernaryNet

## Slide 58: Conclusion
RFML requirements
  High throughput, low latency, good accuracy, integration
We have been working to address ALERT gaps
  Algorithms through cyclostationary sparse FFT [1]
  Latency through PolyLUT-Add [2]
  Edge via integration, ternary networks, quantisation and CSE [3]
  Representations through cyclostationary features [4]
  Training through block minifloat arithmetic [5]

## Slide 59: References (available at https://phwl.org/assets/papers/papers)
[1] Carol Jingyi Li, Richard Rademacher, David Boland, Craig T. Jin, Chad M. Spooner, and Philip H.W. Leong. S3CA: a sparse strip spectral correlation analyzer. IEEE Signal Processing Letters, 31():646–650, 2024.
[2] Binglei Lou, Richard Rademacher, David Boland, and Philip H.W. Leong. PolyLUT-Add: FPGA-based LUT inference with wide inputs. In Proc. International Conference on Field Programmable Logic and Applications (FPL), to appear. 2024.
[3] Stephen Tridgell, David Boland, Philip HW Leong, Ryan Kastner, Alireza Khodamoradi, and Siddhartha. Real-time automatic modulation classification using RFSoC. In 2020 IEEE International Parallel and Distributed Processing Symposium Workshops, IPDPSW 2020, New Orleans, LA, USA, May 18-22, 2020, 82–89. IEEE, 2020.
[4] Carol Jingyi Li, Ruilin Wu, and Philip H.W. Leong. AMD Versal Implementations of
FAM and SSCA Estimators. FPT Conference, 2026 (to appear).
[5] Wenjie Zhou, Haoyan Qi, David Boland, and Philip H.W. Leong. Fpga-based block minifloat training accelerator for a time series prediction network. ACM Trans. Reconfigurable Technol. Syst., December 2025. to appear.